PTC  circuit protection

add: Longhua Town, Bao’an District Shenzhen China

tel: +86-755-61560236-

fax: +86-755-61560237

http://www.szsfhdz.com

email: szfhdz@126.com

RF ®

PTC Resettable Fuse

Made In China

Product ：RF30-135B

No. ：FH-30135-B

Date ：Mar. 03 2007

Redactor ：FuHONG Electronics

AcknowIedged Information

Ⅰ、MARKING:
“RF”——Co-Tech Ele. Logo
“30”——Max Interrupt Voltage
“135”——Maintain Current
“B” ——Product Series
Ⅱ、COAT COLOR:
        ——Yellow
Ⅲ、LEAD MATERIAL :
        ——Lead Plated Copper Clad Steel
Ⅳ、INSULATING MATERIAL:
        ——Cured, Flame Retardant Epoxy Polymer
                meets UL 94 V -0 Requirements
Ⅴ、PRODUCT DIMENSIONS: (mm)

| A (max) | B (max) | C (max) | D (max) |
| --- | --- | --- | --- |
| 8.0 | 10.0 | 3.0 | 5.1 |

Ⅵ、ELECTRICAL CHARACTERISTICS:

| IH (A) | IT (A) | Time-to-trip | V(max) | I(max) | Pd(W) | Rmin(Ω) | Rmax(Ω) |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Trip(A) | T(max) |  |  |  |  |  |
| 1.35 | 2.70 | 6.75 | 3.53 s | 30 | 40 | 0.80 | 0.040 | 0.080 |

Ⅶ、RATE OF TEMPERATURE & IH :

| IH/TEM. | -20 ℃ | 0 ℃ | +20 ℃ | +30 ℃ | +40 ℃ | +50 ℃ | +60 ℃ | +70 ℃ | +80 ℃ |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| RF30-135B | 1.76 | 1.55 | 1.35 | 1.23 | 1.12 | 1.04 | 0.92 | 0.82 | 0.70 |

Ⅷ、PACKING SPECIFICATIONS:

Material used for making packages :   carton

1000 PCS PER BAG;    Bag size : 200 X 140 mm

2000 PCS PER INNER BOX ;  Inner Box size :  205 X150 X 50 mm

20,000 PCS PER OUTER BOX. Outer Box size :  320 X 240 X 280 mm

Ⅸ、GLOSSARY:

Ih: Hold current-maximum current at which the device will not trip at 25℃

It: Trip current-minimum current at which the device will always trip at 25℃

Vmax: Maximum voltage device can withstand without damage at rated

Imax: Maximum fault current device can withstand without damage at rated

Pdmax:  Power dissipated from device when in the tripped state in 25℃ still air

R max: Maximum device resistance at 25℃ prior to tripping

R min: Minimum device resistance at 25℃ prior to tripping

Time-to-trip: Over loading current & time